## Slide 1
HW/SW CO-DESIGN · 00460882
Making Python Fast,
Then Making It Hardware
Profiling two pyperformance benchmarks, optimizing them without changing a single output byte, and proposing an accelerator for each.
Taha Taha · Lana Bakre
Final project · Technion
RESULTS
pyflate
2.51×
raytrace
2.87×
Output byte-identical.
Requirement was 7%.
Measured inside the
course QEMU image.
Notes: Taha. 0:20. Introduce both presenters and the one-line result. Do not explain anything yet.

## Slide 2
THE TASK
Two benchmarks, chosen to disagree with each other
The brief asked for 2 of 13 approved pyperformance benchmarks, ≥7% faster each. We picked a pair that stress opposite parts of the machine — because that is what lets one project motivate both accelerator paradigms from the course.
pyflate
pure-Python bzip2 decompressor
integer, control-flow, irregular memory
variable-length Huffman codes
bits consumed per symbol: 1 to 20
→ data-dependent rate → DATAFLOW
raytrace
pure-Python recursive ray tracer
floating point, allocation bound
every test the same fixed shape
fixed operand count, fixed latency
→ fixed cadence → SYSTOLIC-STYLE ARRAY
A conventional systolic array relies on regular, fixed-cadence data movement. A variable-length stream needs explicit valid/ready flow control to avoid misalignment — which is why pyflate is a dataflow design and ray–sphere intersection is not.
Taha
2
Notes: Taha. 1:20. The key move: the two benchmarks were chosen for contrast, not convenience. End on the bottom strip - it sets up both hardware sections.

## Slide 3
METHOD
No single tool answers both questions
Lecture 4 makes the point directly: a flame graph shows you WHERE, performance counters show you WHY. We used three views, because each one lies in a different direction.
1
py-spy
WHERE
samples PYTHON frames directly;
no -X perf needed
2
cProfile
HOW MANY
call counts, which perf cannot give
— but it charges per call, not per cycle
3
perf stat
WHY
cycles, IPC, cache, branch
— the mechanism behind the speedup
The two profilers disagreed — and that was the useful part.
cProfile charges move_to_front about 10%. py-spy puts it at 15.69% — third overall. Instrumentation charges per CALL; sampling charges per CYCLE. move_to_front rebuilds a list from three slices on every one of its 92,803 calls, so a call-count profiler under-reports exactly that shape. We rewrote the analysis around the sampler.
Taha
3
Notes: Backup B6 carries what perf can and cannot do inside the guest - go there if asked. Taha. 1:10. This is a teaching slide. The disagreement between the two profilers is the point - do not rush the bottom box.

## Slide 4
BENCHMARK 1 · PYFLATE
A bzip2 decompressor written entirely in Python
67,562 compressed bytes in, 399,360 bytes out. The benchmark carries its own MD5, and we used it as the correctness oracle for the whole project.
Huffman
decode
variable-length
prefix codes
Move-to-
front
alphabet reordered
after every symbol
Inverse
BWT
pointer chase
end = T[end]
RLE
expand
runs of ≥ 4
identical bytes
Why a benchmark would implement bzip2 in Python at all
It is deliberate. Calling libbz2 would measure C, not the interpreter. Every import is stdlib — hashlib, struct, os. So this benchmark measures Python executing bit manipulation and table lookups, which is precisely what makes it interesting to optimize and to accelerate.
This also rules out an easy cheat: swapping in libbz2 would have scored a huge speedup while measuring nothing and teaching nothing. We did not do it.
Taha
4
Notes: Taha. 0:50. Keep it short - this is orientation. The last line pre-empts an obvious question.

## Slide 5
BENCHMARK 1 · ANALYSIS
Where the time actually goes
py-spy, cycle-weighted, Python function names. Measured inside the QEMU guest.
decode_huffman_block
21.79%
find_next_symbol
16.54%
move_to_front
15.69%
readbits
9.71%
snoopbits
9.25%
bwt_transform
9.01%
bwt_reverse
6.16%
_mask
3.70%
GROUPED BY STAGE
42.0%
Huffman decode
15.7%
Move-to-front
15.2%
Inverse BWT
21.8%
decode loop body
3,185,454 Python function calls to decompress 400 KB. That is the number to keep in your head for the next slide.
Taha
5
Notes: Taha. 1:10. Read the top three. Flag that move_to_front is second - that is the perf-vs-cProfile disagreement showing up. End on the call count.

## Slide 6
BENCHMARK 1 · THE TURNING POINT
The obvious diagnosis was wrong
find_next_symbol() walks a sorted table linearly, so everyone's first conclusion is "the scan is too deep". We almost optimized the wrong thing.
148,271
calls to find_next_symbol
341,601
calls to snoopbits
2.3
probes per symbol — not ~250
Why: move-to-front keeps the hot symbols on short codes, so the scan almost always exits after two probes.
So the cost was never scan depth. Decoding ONE symbol cost about seven Python function calls: find_next_symbol, ~2.3 snoopbits, a readbits, and several _mask. The fix had to remove CALLS, not iterations — the opposite of what the benchmark's own source comment suggests.
Taha
6
Notes: Taha. 1:30. THE most important slide in the pyflate half. Pause after '2.3, not 250'. If short on time elsewhere, protect this slide.

## Slide 7
BENCHMARK 1 · THE THREE IMPLEMENTATIONS
One Huffman symbol, three ways
Same bzip2 stream, same decoded byte. What changes is how much work one symbol costs — and how much of it happens at once.
A BASELINE SOFTWARE
B OPTIMIZED SOFTWARE
C HARDWARE ACCELERATOR
Walks a sorted list of HuffmanLength objects
Re-peeks the stream at every new candidate length
~7 Python calls per symbol, 2.3 stream peeks
limit / base / perm tables replace the scan
Starts at min_len = 2, extends one bit at a time
Bit cursor in locals — no calls in the hot loop
bit_window exposes the next 20 bits
20 comparators test lengths 1–20 at once
Priority encoder takes the shortest match
valid / ready retires sym_len bits
A CODE THAT IS 5 BITS LONG
Scans candidates, peeking at the stream again at each new length
A CODE THAT IS 5 BITS LONG
Tests 2 → 3 → 4 → 5 in sequence, with no function calls
A CODE THAT IS 5 BITS LONG
Tests 1…20 at once, selects 5, retires 5 bits on the handshake
sequential on the CPU
sequential — 2.27× fewer instructions
1 symbol / cycle · 800 MHz target
MEASURED · inside the course QEMU guest
1115 ms → 445 ms · 2.51× faster · t = 676 · output byte-identical (MD5 over 399,360 bytes)
ESTIMATED · not an end-to-end measurement
~0.7 ms of on-chip time: 148,271 symbols at 1/cycle (~185 µs) plus a 399,360-cycle chase (~499 µs) at 800 MHz. Assumes the block is already in on-chip SRAM; excludes DMA, driver and IOMMU setup.
Prefix-free codes make the shortest match the correct one. A variable-length stream needs valid/ready to control when state advances — the 20 comparisons happen every cycle regardless, so the handshake never serializes them.
Taha
7
Notes: Taha. 1:30. Read it left to right. BASELINE: the decoder walks a sorted list of Huffman objects and re-peeks the bitstream whenever the candidate length changes - about seven Python calls to decode one symbol. The profile is what pointed here: 148,271 symbols produced 341,601 peeks, only 2.3 per symbol, so the bottleneck is CALL COUNT, not scan depth. OPTIMIZED: the codes are already canonical, so limit/base/perm let us start at the minimum length and extend one bit at a time, and the bit cursor lives in local variables, so the hot loop makes no Python calls at all. Still one length at a time, still one core - 2.27x fewer instructions is where the 2.51x comes from. HARDWARE: the window exposes 20 bits, twenty comparators test every length simultaneously, and a priority encoder takes the shortest match, which prefix-free codes guarantee is the correct one. Be explicit about the two bottom boxes: 1115 to 445 ms is MEASURED in the guest; the 0.7 ms is an ESTIMATE under the assumptions printed there. Likely question: 'does the valid/ready handshake serialize your twenty comparators?' Answer: no - all twenty comparisons happen every cycle; the handshake only decides when the window retires bits and the symbol moves on. Second likely question: 'why not a systolic array?' Because the number of bits consumed per symbol is data-dependent, so a fixed-cadence array would mis-align; the parallelism comes from the comparators, the flow control from valid/ready.

## Slide 8
BENCHMARK 1 · RESULT
2.51× faster — and the counters say why
1115 ms
baseline
445 ms
optimized
2.51×
60.1% cut · t = 676
pyperf --rigorous
inside the QEMU guest
pinned with taskset
baseline
optimized
ratio
cycles
8.30 G
3.30 G
2.51× fewer
instructions
21.56 G
9.49 G
2.27× fewer
IPC
2.60
2.87
+10% only
cache-misses
2.78 M
526 K
5.3× fewer
IPC barely moved. The machine did not get smarter — it was asked to do less.
Cycles fell 2.51x and runtime fell 2.51x — the counters and the stopwatch agree. Instructions fell 2.27x while IPC gained only 10%, so the speedup is 2.27 × 1.10 = 2.50: overwhelmingly execute-fewer-instructions. The win came from deleting interpreter work, not microarchitectural cleverness.
Taha
8
Notes: Taha. 1:20. Land the IPC row. This is the strongest single piece of evidence in the whole project - instructions fell in near-exact proportion to the runtime.

## Slide 9
BENCHMARK 2 · RAYTRACE
A recursive ray tracer, 100×100, eight objects
One large sphere, six small spheres, a checkerboard plane, two point lights. Lambert diffuse plus a specular reflection, recursing to depth 3.
per pixel:
build primary ray → normalized() [sqrt]
test against all 8 objects → nearest hit
shade it:
1 reflection ray → recurse
2 lights × shadow rays → 8 objects each
18
intersection tests per pixel
Not 8. The extra ones are shadow rays and reflection rays — 179,457 calls for 10,000 pixels. Intersection is THE kernel, and that is what we later put in hardware.
Why this one, next to a decompressor
pyflate is integer and control-flow bound. This is floating point and allocation bound. Same interpreter, opposite bottleneck — and, as we will show, opposite accelerator.
Lana
9
Notes: Lana. 0:50. Your opening - re-establish yourself. The 18-per-pixel number is the hook; it justifies the hardware choice later.

## Slide 10
BENCHMARK 2 · ANALYSIS
Half the runtime is in three-float wrappers
dot
18.58%
__sub__
15.71%
__init__
15.19%
intersectionTime
11.81%
_lightIsVisible
8.00%
scale
4.42%
normalized
3.06%
magnitude
2.78%
59.74%
of runtime is in Vector/Point wrappers (orange bars), not in the ray tracing algorithm itself
509,871
calls to Vector.dot — every one of them starts with a mustBeVector() type assertion
The leaves of this flame graph are type checks and operator dispatch — not floating-point work. 309 function calls per pixel.
Lana
10
Notes: Lana. 1:10. Point at the orange bars as a group - that is the 47%. The dynamic type checks cost more than the arithmetic they guard.

## Slide 11
BENCHMARK 2 · THE FINDING
One line, in the wrong place, cost 44%
BEFORE
for (o, s) in self.objects:
t = o.intersectionTime(
Ray(p, l - p)) ← inside
AFTER
shadowRay = Ray(p, l - p) ← hoisted
for (o, s) in self.objects:
t = o.intersectionTime(shadowRay)
Ray(p, l - p) does not depend on o. Its constructor calls normalized() → magnitude() → sqrt(). So the same shadow ray, square root included, was rebuilt 8 times per light per shading point.
+44%
slower when we revert just this one hoist. A three-line change, with no cleverness in it at all.
The lesson
This is a plain bug, not a subtle trade-off — and reading the code at normal speed does not reveal it. Profiling did. That is the whole argument for measuring before optimizing.
Lana
11
Notes: Lana. 1:20. Your strongest slide. Let the before/after sit for a beat before saying 49%. Protect this slide if running late.

## Slide 12
BENCHMARK 2 · THE THREE IMPLEMENTATIONS
One ray–sphere test, three ways
Same intersection, same image, bit for bit. The algorithm never changes — the cost of expressing it does, and then who performs it.
A BASELINE SOFTWARE
B OPTIMIZED SOFTWARE
C HARDWARE ACCELERATOR
Vector / Point objects; every op type-checks
509,871 mustBeVector() calls per frame
Shadow ray rebuilt inside the object loop
Shadow ray hoisted out of the loop — +44%
Intersection inlined on raw floats — +56%
radius² cached; running minimum, no list — +8%
Operand order preserved → bit-identical
8 PEs, one sphere each, preloaded per frame
Fixed shape: 7 multiplies, 9 add/sub, 1 sqrt
Ray broadcast to all 8, results captured together
Shared 24-stage sqrt → 1 ray / 8 cycles
ONE RAY AGAINST EIGHT SPHERES
Eight tests, each dragging a cascade of wrapper calls behind it
ONE RAY AGAINST EIGHT SPHERES
The same eight tests, on raw floats, with nothing allocated
ONE RAY AGAINST EIGHT SPHERES
All eight at once; replicate the sqrt for 1 ray/cycle at ~8× its area
59.74% of runtime in float wrappers
sequential — 2.78× fewer instructions
intersection kernel only — shading stays on the CPU
MEASURED · inside the course QEMU guest
809 ms → 282 ms · 2.87× faster · t = 315 · image bit-identical at seven resolutions
ESTIMATED · not an end-to-end measurement
~22 µs of array time per frame: 179,457 tests as ~22,432 ray-groups at 1 ray / 8 cycles, 1 GHz. Ray generation, shading and recursion stay on the CPU, and transfer overhead is excluded.
Amdahl bounds it: intersection is 35.03% of the OPTIMIZED runtime, so even an infinitely fast unit caps a whole frame at 1 / (1 − 0.3503) = 1.54×.
Lana
12
Notes: Lana. 1:30. Left to right again. BASELINE: the renderer is written with Vector and Point objects, so every subtraction and dot product is a method call that first type-checks its operand - 509,871 of those checks in one frame - and each one allocates a temporary. Worse, the shadow ray is constructed INSIDE the loop over objects, so the same ray, square root included, is rebuilt eight times per light. That single line is the bottleneck the profile found. OPTIMIZED: hoist the shadow ray out of the loop, inline the intersection arithmetic on raw floats, cache radius squared, and track the nearest hit with a running minimum instead of building a list. The ablation numbers on the slide are what each change is worth. Critically, we kept the floating-point operand order, so the image is bit-identical - a speedup that changed a pixel would be worth nothing. HARDWARE: the kernel is the same shape every time, so eight processing elements each hold one sphere, preloaded once per frame, and the ray is broadcast to all of them; they compute in parallel and the nearest hit is reduced on the way out. The sqrt is the real design decision: shared, it sets one ray per eight cycles; replicated, one ray per cycle for about eight times the sqrt area. Be explicit: 809 to 282 ms is MEASURED; the 22 microseconds is an ESTIMATE. And state the Amdahl line yourself before anyone asks: intersection is 35% of the optimized runtime, so the whole-frame ceiling is 1.54x - the hardware replaces the kernel, not the renderer.

## Slide 13
BENCHMARK 2 · RESULT
2.87× faster — and a trap in reading counters
809 ms
baseline
282 ms
optimized
2.87×
65.1% cut · t = 315
IPC 2.59 → 2.70
instructions 2.78× fewer
Same story as pyflate.
One row looks like a regression — and is not
cache-miss RATE
1.02%
2.91%
WORSE
cache REFERENCES
18.7 M
3.00 M
6.23× fewer
cache MISSES
190 K
87 K
2.18× fewer
The optimized code makes 6.23× fewer cache REFERENCES, because it no longer allocates and chases a swarm of short-lived Vector objects. The references that remain are the genuinely cold ones — so the ratio of misses to references rises even though the machine stalls far less often.
This is the same trap the course's own perf tutorial sets with row-major vs column-major traversal. A rate is not a performance metric; misses per unit of work is.
Lana
13
Notes: Lana. 1:20. Tie it explicitly to tutorial 2 - row vs column major. Staff will recognize their own example and it shows we connected the material.

## Slide 14
BENCHMARK 2 · HARDWARE
The square root is the real design decision
Not the multipliers. fp32_sqrt is 24 pipeline stages — by far the largest block — so whether it is shared or replicated sets both the throughput and roughly half the array area.
Shared (what we built)
1 sqrt unit · 1 ray / 8 cycles
Smallest area. The sqrt sets the throughput: 8 spheres must drain through one pipeline before the next ray enters.
Replicated (also buildable)
8 sqrt units · 1 ray / 1 cycle
8× the throughput for roughly double the total array area. The design is parameterized, so both points on the curve are real.
A second knob: accuracy against area
Our root truncates rather than rounds. Measured against math.sqrt over 6,008 samples: 1.16 ulp worst case. A 25th stage plus a rounding incrementer brings that to 0.69 ulp. We kept truncation, because 1 ulp of a distance cannot move an 8-bit colour channel — but it does mean this accelerator is NOT bit-exact, unlike the pyflate one.
And one place where precision is not negotiable: bfloat16 would halve the multiplier area, but 8 mantissa bits cannot survive the cancellation in (cc − v·v). We rejected it.
Lana
14
Notes: Lana. 1:00. The brief asks for performance/area/power trade-offs - this slide IS that requirement. If late, state the shared-vs-replicated trade and skip the ulp numbers.

## Slide 15
VERIFICATION
We simulated the RTL — and it was wrong
tb_ray_sphere failed on its second test vector
2 + 3 → 6.5 9 − 4 → 2.5
fp32_add had two coupled off-by-one errors: the carry path normalized the leading one to bit 26 while the leading-zero path normalized it to bit 27 — and the mantissa slice matched neither convention. The module had been written carefully and reviewed. It was still flatly wrong.
Three hand-picked vectors were enough to MISS it, so we added 400 randomized ones — a quarter of them near-cancelling subtractions, the case that exercises the long normalize path where the bug lived. It happened again later: a rewritten BWT chase looked right and ran at two cycles per hop until its new testbench caught it.
correctness gate — byte / bit-identical
extended — 16 streams vs libbz2
golden model — 148,271 symbols
sqrt model — 6,008 samples
tb_huffman_decoder — symbol + bits
tb_bit_window — 12 retires, 1 to 20 b
tb_mtf_unit — pre-move entry
tb_run_expander — RUNA/RUNB + stall
tb_rle_final — outer RLE, zero count
tb_bwt_index_builder — T[] vs software
tb_bwt_reverse — chase vs software
tb_top_block — END TO END, whole block
tb_ray_sphere — single PE, bit-exact
tb_ray_array — nearest of 8 spheres
tb_fp_random — 400 vectors, bit-exact
15 / 15 green in the guest · ./tools/regress.sh
Lana
15
Notes: Lana. 1:00. Do not hide this - a found bug is evidence the verification works. Say plainly: we wrote it carefully, reviewed it, and it was wrong on vector two. If asked what tb_top_block covers: the assembled accelerator is programmed through its CSRs like a driver would, fed one compressed block, and checked byte for byte - plus both Rule 3 refusals (randomised block, block bigger than the on-chip index memory).

## Slide 16
SYNTHESIS
Two benchmarks, two paradigms
This is why we chose the pair we did. The same project motivates both of the dominant accelerator patterns from the course — and, more importantly, shows why each one is wrong for the other workload.
pyflate
raytrace
Bound by
integer, control flow, memory
floating point, allocation
Data rate
VARIABLE — 1 to 20 bits/symbol
FIXED — same shape every test
Pattern
DATAFLOW, valid/ready
SYSTOLIC-STYLE, weight-stationary
Key idea
20 comparators + priority encoder
preload spheres, stream rays
Bit-exact?
yes
no — truncating sqrt, 1.16 ulp
A conventional systolic array moves data at a fixed cadence, so a variable-rate bitstream mis-aligns it. pyflate therefore needs valid/ready flow control; the fixed-shape intersection kernel does not.
Taha + Lana
16
Notes: Both. 0:40. Taha reads the pyflate column, Lana the raytrace column, then one of you reads the bottom strip. Rehearse the handoff.

## Slide 17
LIMITATIONS
What we did not finish
Stating this plainly is deliberate. Every claim in our reports is one we can defend; these are the ones we cannot.
1
End-to-end simulation covers a SMALL block, not the benchmark file
tb_top_block programs the accelerator through its CSRs, streams one compressed block in and checks the bytes that come out - so the assembled design does decompress. But the block is 15 bytes, generated by running the bzip2 encoder in Python. Feeding interpreter.tar.bz2 through the RTL would need a full driver model and a long simulation.
2
One Huffman table at a time - the biggest gap to a usable accelerator
A real block carries up to six tables and switches every 50 symbols. The hardware holds one set, so the driver would reprogram it at each switch - roughly 3,000 bursts for the benchmark block. A production design holds six banks and selects with the decoded selector stream.
3
Amdahl caps both accelerators
raytrace intersection is 35% of the optimized runtime → 1.54× ceiling on a whole frame. For pyflate, a 67 KB input behind PCIe would be dominated by the round trip — which is why this belongs on-die, not on a discrete card.
Taha
17
Notes: Taha. 0:25. Move briskly - do not dwell. Volunteering limitations pre-empts the question and reads as confidence, not weakness.

## Slide 18
SUMMARY
Requirement was 7% on two benchmarks
pyflate
1115.1 ms
444.6 ms
60.1%
2.51×
t = 676.00
raytrace
809.3 ms
282.2 ms
65.1%
2.87×
t = 315.11
Measured inside the course QEMU guest. Both clear the bar by roughly 9×, both statistically significant, and both with output identical to the original — byte for byte for pyflate, pixel for pixel for raytrace.
What we would want you to take away
In both benchmarks the obvious diagnosis was wrong, and the counters — not intuition — settled it. Cycles fell in step with the stopwatch while IPC barely moved. We did not make the machine faster; we stopped asking it to do work that was never needed.
Lana
18
Notes: Lana. 0:15. Short. Then: 'Happy to take questions, and we have the code running if you would like to see anything.'

## Slide 19
END OF PRESENTATION
Thank you
Questions welcome — the code runs, and we can open any file, flame graph or testbench you would like to see.
Taha Taha · Lana Bakre
HW/SW Co-design · 00460882 · Technion
RESULTS
pyflate
2.51×
60.1% less time
raytrace
2.87×
65.1% less time
15 / 15 checks green inside the course QEMU guest
pyflate byte-identical over all 399,360 bytes · raytrace bit-identical at seven resolutions · the bzip2 accelerator decompresses a whole block end to end in simulation
Backup slides follow — B1 to B5
Taha + Lana
19
Notes: Both. 0:05. Stop here - this is the end of the presented material. Leave the slide up for the questions: it carries both headline numbers and the verification count. Everything after it is backup: B1 canonical Huffman, B2 the three interface rules, B3 the measurement environment, B4 what we rejected, B5 testing beyond the benchmark.

## Slide 20
BACKUP B1
Canonical Huffman: why limit/base/perm works
BACKUP — not presented
populate_huffman_symbols() already assigns canonical MSB-first codes — codes handed out in increasing order, shifted left whenever the length grows. That structure is what the linear scan ignores.
zvec = next min_len bits
while zvec > limit[zn]:
zn += 1
zvec = (zvec << 1) | next_bit
sym = perm[zvec - base[zn]]
Worked example (6 symbols)
lengths [2,2,2,3,4,4]
sym 0→00 1→01 2→10
sym 3→110 4→1110 5→1111
limit[2]=2 base[2]=0
limit[3]=6 base[3]=3
limit[4]=15 base[4]=10
These are the exact vectors in tb_huffman_decoder.v. The testbench checks both the decoded symbol and the number of bits retired — a decoder that returns the right symbol while consuming the wrong number of bits destroys the rest of the stream.
backup
20
Notes: If asked how canonical decoding works, or how the hardware table is built.

## Slide 21
BACKUP B2
Host/software interface and the three rules
BACKUP — not presented
Rule 1
Do not expect users to change their code
Python still calls bz2.decompress(). Nothing above the library moves.
Rule 2
If software must change, confine it to the library
Only the decompressor gains a fast path: map buffers, push the Huffman tables through the CSR window, write CTRL.START, sleep on the interrupt.
Rule 3
Never break the user's code
START returns UNSUPPORTED for a randomised block or one larger than the on-chip SRAM, and the driver falls back to software. Our optimized Python mirrors this: a gzip input falls back to the baseline decoder.
Security: the accelerator is a DMA master behind the IOMMU, with per-device page tables, so it can only touch the buffers the driver mapped for that request.
backup
21
Notes: If asked about the HW/SW interface, the driver, or security.

## Slide 22
BACKUP B3
Measurement environment
BACKUP — not presented
where
INSIDE the course QEMU image — systemd-detect-virt = kvm
distro
Ubuntu 22.04.5 LTS, kernel 5.15.0-1080-kvm
guest
8 vcpus, 3938 MB, Haswell vPMU
python
CPython 3.10.12 · pyperf 2.10.0 · perf 5.15.179
profilers
py-spy 0.4.2 (Python frames) · cProfile (call counts)
simulator
Icarus Verilog 11.0
launch
-cpu host,pmu=on over a qcow2 overlay; image never written
method
pyperf --rigorous, taskset -c 2, counters in groups of two
pmu=on is what makes hardware counters work at all in the guest; without it perf answers <not supported> for every hardware event. Every table in both reports regenerates with ./script_pyflate.sh and ./script_raytrace.sh, run inside the guest.
backup
22
Notes: If asked where the numbers came from, or about measurement noise.

## Slide 23
BACKUP B4
Things we tried and rejected
BACKUP — not presented
✗
A full 2^20-entry Huffman LUT
Would decode in one step, but bzip2 allows 6 tables of length ≤ 20 — about 6M entries to BUILD per block, for a block that decodes 148k symbols. Table construction costs more than it saves.
✗
numpy for the inverse BWT
An added dependency for a stage the ablation shows is worth ~3%.
✗
A BVH for raytrace
The first thing a graphics person proposes. With 8 objects, traversal overhead exceeds the 8 intersection tests it would save.
✗
bfloat16 in the raytrace datapath
Halves multiplier area, but 8 mantissa bits cannot survive the catastrophic cancellation in (cc − v·v).
✗
Swapping in libbz2 / a C extension
Would post a huge speedup while measuring nothing. The benchmark exists to measure the interpreter.
backup
23
Notes: If asked 'did you consider X'. Most likely question of the whole session.

## Slide 24
BACKUP B5
How we tested beyond the benchmark
BACKUP — not presented
pyflate — 16 streams vs libbz2
empty, 1 byte, 1 KB of zeros, RLE runs
highly repetitive, text, 64 KB random
a 900 KB MULTI-BLOCK file
levels 1 and 9, both round-tripping
checked against libbz2, not our own baseline
raytrace — 7 resolutions
2×2, 3×7, 16×16, 50×50
100×100, 101×37, 128×96
bit-identical at every one
the default is not a special case
Two API divergences we found and disclosed
Removing the type assertions (O3) means Vector − Point and Vector.dot(Point) now compute silently where the baseline raised TypeError. Both are invalid usage the renderer never produces — but they are a behaviour change, so we documented them rather than leaving them to be discovered.
The correctness gate runs before any timing is reported. tools/verify.py compares all 399,360 decompressed bytes and the full 30,000-byte framebuffer.
backup
24
Notes: If asked whether the optimization generalizes, or only works on the one benchmark file.

## Slide 25
BACKUP B6
What perf can and cannot do inside the guest
BACKUP — not presented
All of our work runs inside the course QEMU image. That constrains the tooling in ways we had to establish by testing, not by assuming:
qemu-system-x86_64 -m 4096 -smp 8 -cpu host,pmu=on -accel kvm ...
Counting works — only because of pmu=on
Without that flag the guest has NO virtual PMU and perf answers <not supported> for every hardware event. With it we get a Haswell vPMU: cycles, instructions, cache and branch counters all count.
This is the only reason we have counter data at all.
Sampling does NOT work
perf record on a hardware event captures ZERO samples here, even though perf stat counts that same event fine. Counting and sampling are different paths and only counting is virtualized.
Fix: flame graphs use -e cpu-clock, which is timer-based.
The trap that nearly went into the report as a fact
Our first pass asked perf stat for six events at once. cycles came back as exactly 0, and we almost wrote "cycles is unsupported in the guest". It is counter multiplexing: the guest has fewer usable counters than a bare machine. In groups of two, cycles reads fine. Also: CPython 3.10 predates -X perf, so perf cannot name Python functions here — py-spy does that instead.
backup
25
Notes: Backup. Use if asked how we measured inside the VM, why the flame graphs use cpu-clock, or why there is no CPI stack. The cycles=0 story is the strongest bit - we nearly published a wrong fact.